## Slide 1: BGP

## Slide 2: BGP Introduction
The Border Gateway Protocol (BGP, RFC 1771) is a highly scalable, powerful interdomain routing protocol used by:
  corporate networks to connect to their ISPs
  ISPs for connection with other ISPs.
The most recent implementation is BGPv4, which supports CIDR:
  reduced the size of ISP backbone routing tables
  allowing the explosive expansion in the Internet since BGPv4’s introduction in March 1995.
Notes: EGP3不能处理路由环路和路由策略。所以被BGP4取代。
画第一页

## Slide 3: Autonomous Systems
An autonomous system is defined in RFC 1771 as:
  a set of routers under a single technical administration, using and interior gateway protocol and common metrics to route packets within the AS, and using an exterior routing protocol to route packets to other ASes.
Notes: 不同组织的路由安全策略可能会有冲突。AS中可以有多个IGPs

## Slide 4: IBGP and EBGP
ISPs will often use BGP exclusively within and without its own AS.
  When BGP is run inside an AS, it is called internal BGP or IBGP.
  When BGP is run between ASes, it is called external BGP or EBGP.
Other ASes find BGP lacks flexibility as an IGP, so they will implement additional IGPs such as RIP or OSPF.
Notes: 画图（第三页）表示其区别，说明：
多条路径时，只选最优的使用
只告知邻居自己使用的路由
BGP speaker 从EBGP学习的路由告诉给EBGP和IBGP
BGP speaker 从IBGP学习的路由不告诉给IBGP；是否告诉EBGP由同步情况来确定
同步

## Slide 5: AS Number
The AS number: a 16 bit field
  Like public IP addresses, you must obtain a public AS from either your service provider or directly from IANA.
  Like private IP addresses, there is also a range of private AS numbers that any AS can use to route between itself and its ISP.
    Like NAT’s stripping of private IPs, the ISP will strip the private AS number and apply a public AS number.
Notes: IANA: Internet Assigned Numbers Authority.
64512-65535 私用

## Slide 6: Private AS Number
When the AS number used is private, the first six high order bits in the AS field will all be set to 1.

## Slide 7: AS and External Connections(I)
An AS can be classified by number of connections to ISPs:
  A Single-homed AS: has one exit to the ISP
  A Multi-homed AS: has multiple exits to the ISP(s) and can be further classified as...
    Non-transit ASes: do not allow routing of traffic from one ISP connection to another ISP connection.
    Transit ASes: allow traffic to be routed from an external AS, through the local AS, to another AS.

## Slide 8: AS and External Connections(II)
A Single-homed AS
  BGP is not required in a single-homed AS
  Instead of BGP, the AS will set a default route to the ISP and the ISP will set static routes to all the AS’s internal networks
A Multi-homed AS
  Non-transit ASes
    This would be the desired configuration for a multi-homed corporate AS
  Transit ASes
    ISPs are multi-homed transit ASes
    Routing of transit traffic is done by routers configured as IBGP routers; also called transit routers.
Notes: Static
IGP，由于本地网络稍复杂
由私有AS号配置单宿主

## Slide 9: When to Use BGP?
When not to use BGP
  The local AS’s routing policy does not differ from the external AS’s (ISP).
  The AS is a single-homed AS
When to use BGP
  The AS is a transit AS for other ASes
  The AS has multiple connections to other ASes
  The flow of traffic entering and leaving the AS must be manipulated with policy-based routing configuration

## Slide 10: Policy-Based Routing
BGP is a policy-based routing protocol.
  Although it is considered an advanced distance vector routing protocol, BGP has many configurable path vectors (or attributes).
Network policy decisions define exactly how BGP routing information should be controlled as it passes from one AS to another.
  These policies can be quite complex, requiring the network administrator to be fully conversant in the way BGP operates
Notes: As_path：DV

## Slide 11: BGP: Using TCP
BGP uses a TCP connection to
  establish peer relationships with other BGP routers
  transmit all BGP traffic.
Since TCP is required, the only protocol stack allowed on the Internet is TCP/IP.
  Traffic from other stacks (e.g. IPX/SPX) must be translated into TCP/IP traffic at the ASBR before propagating to the Internet
Notes: Peer：虚连接，但如果不同步则可能实际不可达。可靠传输

## Slide 12: BGP Segment
A BGP encapsulated segment
  Note: BGP uses TCP port number 179
6 – TCP
17 - UDP
179 – BGP
23 – Telnet
80 - HTTP

## Slide 13: BGP Operation
Once a TCP connection is established between two BGP peers, each will transmit an OPEN message to negotiate and confirm the BGP connection parameters.
Some of the parameters negotiated include:
  BGP version number
    Both peers must run the same version; can be negotiated if one peer is running an earlier version than BGPv4.
  AS number
    The sender’s AS number must match the receiving routers neighbor statement (more on this later).
Notes: 解释同步问题

## Slide 14: BGP Operation
  Hold Time
    The max. time to elapse without a keepalive; Two peers negotiate the smallest of their configured holdtimes.
  BGP router ID
    Sender’s router ID must match the receiving router’s neighbor statement (more on this later).
    Chosen exactly like OSPF: highest active interface or highest loopback.

## Slide 15: BGP Operation
BGP peers uses four separate message types. These BGP packets, briefly described, are...
  OPEN—establishes the peer relationship; if disagreements, a NOTIFICATION is sent and connection does not get established.
  UPDATE—after the initial exchange of routing information, BGP only updates when there’s a topology change.
  KEEPALIVE—interval negotiated during establishment phase; keeps peer relationship established.
  NOTIFICATION—used when an error is found in a message received; returns the connection to idle.
Notes: Update：增量更新

## Slide 16: BGP Neighbor Negotiation
Neighbor negotiation: six distinct states
  Idle: waiting for a start event
    system initializes a TCP connection and sets a local ConnectRetry timer.
  Connect: waiting for the TCP connection to be completed
    If successful:
      send an OPEN message
      move to the Open Sent state
    If fails:
      reset the ConnectRetry timer
      proceed to the Active state
      listen for a TCP connection initialized by a BGP peer
    If the ConnectRetry timer expires: reset it and again and try to initiate a TCP connection; state remains in Active.
    Any other event will return the state to Idle.
Notes: 画一下状态机
idle启动后，发起一个tcp连接，并开始侦听tcp连接，即进入连接状态
Connect：等待连接完成

## Slide 17: BGP Neighbor Negotiation
  Active: system is trying to acquire a peer by initiating a TCP connection.
    If successful: send an OPEN message and move to the Open Sent state
    If ConnectRetry timer expires: return to Connect.
  Open Sent: Waiting for an OPEN message from the peer
    When OPEN is received, it is checked for errors (e.g. bad version, wrong AS #, etc.)
    If errors are detected, a NOTIFICATION message is sent and the state is changed to Idle.
    If all is well, hold timer is negotiated and KEEPALIVES are sent
Notes: 可能会在active和connect之间变换，因为tcp连接没有生效。
Open sent：根据AS确定是IBGP还是EBGP，待到tcp失效后，会退回到active

## Slide 18: BGP Neighbor Negotiation
  Open Confirm: waiting for either a KEEPALIVE or NOTIFICATION.
    If a KEEPALIVE is received: change to Established
    If the Hold Timer expires: send a NOTIFICATION and returns the state to Idle
    If the system receives a NOTIFICATION: return to Idle
  Established: exchange UPDATE, KEEPALIVE, and NOTIFICATION messages with its peer.
    If receives an UPDATE or KEEPALIVE: reset its Hold Timer unless the timer is set to zero.
    If receive a NOTIFICATION message: return to Idle.
    The system sends a NOTIFICATION message and returns the state to Idle when...
      The Hold Timer expires or
      An error is detected in a received UPDATE message
Notes: Established：开始交换路由

## Slide 19: The BGP Packet Header
All BGP messages contain the same required BGP packet header.
  16 byte Marker field
  2 byte Length field
  1 byte Type field
Data following the packet header can add 0 bytes up to an additional 4,077 bytes for a total acceptable length of 4096 bytes.

## Slide 20: Type 1: OPEN
All the parameters must be agreed upon by the peers before session establishment can occur.
The Optional Parameters can include things such as Authentication.

## Slide 21: Type 2: UPDATE
  The minimum length is 23 bytes.
    19 bytes for the BGP packet header
    2 bytes for Unfeasible Routes Length
    2 bytes for Total Path Attributes Length
  Unfeasible Routes Length specifies the size, in bytes, of Withdrawn Routes.
    Withdrawn routes are expressed in the length/prefix format
      length is a byte specifying the prefix length in bits (CIDR notation)
      For example, 10.1.1.0/24 would have a length of 24 and a prefix of 10.1.1.0
  Total Path Attributes Length specifies the size, in bytes, of Path Attributes.
  Network Layer Reachability Information (NLRI) contains a list of IP address prefixes reachable through the advertising router.
Notes: 每个update报文里面的属性序列要是一样的，如果不一样要分成几个update报文。
NLRI:网络层可达信息

## Slide 22: Type 3: NOTIFICATION
The NOTIFICATION message is sent whenever an error is detected and the BGP connection is then immediately closed.
  Error Code: specifies the type of NOTIFICATION and the Subcode field provides more specific information about the nature of the reported error.
    For example, Error code 2 with an Error subcode of 2 will translate as “Bad Peer AS” meaning that you configured the wrong AS for the peer.
Notes: Data为与error有关的数据，如出错的AS号等

## Slide 23: Type 4: KEEPALIVE
It is simply a 19 byte BGP Packet Header.
The KEEPALIVE has no other data.
Keepalives are sent, by default, every 60 seconds.
In the Cisco IOS, the Hold Timer is 3 times the Keepalive interval.
Keepalives are used between peers once the connection has become fully negotiated and established.
An UPDATE message will also reset the Hold Timer.

## Slide 24: Path Attributes Overview
The UPDATE message contains a list of path attributes for the route being advertised in the NLRI field:
  The first 3 high order bits of the Attribute Flags field specify whether the attribute is well-known mandatory, well-known discretionary, optional transitive, or optional non-transitive.
  The fourth high order bit specifies the length of the Attribute code. The remaining bits are unspecified and are set to 0.
  In the Cisco IOS, the Attribute Code contains 1 of 10 types; seven supported by all implementations of BGP and three Cisco-specific.
Notes: 本页重点描述path attributes field的结构
Mandatory：公认必遵属性
Discretionary：酌？公认自决
optional transitive：任选可传递
第三个bit指示任选可传递属性中的信息是部分的1还是完整的0
第四个bit指示属性长度是1字节还是2字节。
标志位其他4位都置0

## Slide 25: Path Attributes Overview
Path Attributes are divided into four categories:
  Well-known Mandatory
    attribute must be included in all implementations of BGP; if missing in the UPDATE message, a NOTIFICATION error message is sent
  Well-known Discretionary
    attribute is recognized by all implementations of BGP but may not be sent in an UPDATE message
  Optional Transitive
    attribute may not be recognized by all implementations of BGP but should be sent to BGP peers.
  Optional Non-transitive
    attribute may not be recognized by all implementations of BGP. If not recognized it is ignored. Whether recognized or not, it is removed from UPDATE messages sent to BGP peers.
Notes: 解释四个属性类型的差别
公认必遵属性：每条路由都必须携带的属性，如果没有则该路由为非法
公认自决属性：可携带可不携带的属性
任选可传递属性：老版本路由器不支持新版本的属性，但是转发
任选不可传递属性：路由器收到后如果不能识别则不作转发

## Slide 26: Path Attributes Overview
The 10 attributes used by the Cisco IOS are summarized below.
Notes: 现在已用了16种属性，可扩展到256种

## Slide 27: ORIGIN
ORIGIN: a well-known mandatory attribute
ORIGIN specifies how the advertising router learned about the route listed in the NLRI field.
  In BGP decision-making process, preferring routes with a lower ORIGIN value.
    Thus: IGP over EGP; EGP over Incomplete
  One byte long
Notes: 起点属性：记录一条路由如何成为BGP路由
IGP：路由发源地在AS内部
Incomplete：路由由redistribute注入，路由起源未知，后来又发布到BGP中
EGP：通过某种外部网关协议如BGP发现的路由

## Slide 28: AS_PATH
AS_PATH: a well-known mandatory attribute
AS_PATH is is composed of a sequence of AS path:
  Path Segment Type (1 byte)
    Value 1 = AS_SET: an unordered set of ASes that the route has traversed is contained in the Path Segment Value
    Value 2 = AS_SEQUENCE: an ordered set of ASes that the route has traversed is contained in the Path Segment Value
  Path Segment Length (1 byte)
    specifies the number of ASes in the Path Segment Value
  Path Segment Value
    2 bytes for each AS the route has traversed (AS is a 16 bit number)
AS_PATH is similar to Hop Count
  All other attributes being equal, BGP will choose the shortest AS_PATH
Notes: 路由在传播中都经过哪些自治系统
顺序经过画图：
18.0.0.0/8
AS sequ 4 1 被选，因为较短
AS sequ 3 2 1
Set经过画图：18.1.0.0,18.2.0.0,18.1.0.0经过AS4被聚集为18.0.0.0
18.0.0.0/8
4{1 2 3} AS SET 4，AS SET 1 2 3

## Slide 29: NEXT_HOP
NEXT_HOP: a well-known mandatory attribute
NEXT_HOP defines the IP address of the border router that should be used as the next hop.
  For EBGP sessions the NEXT_HOP will be the advertising router’s own IP address.
  For IBGP sessions the NEXT_HOP of an EBGP route is advertised into the AS with the NEXT_HOP unchanged.
    Therefore, internal BGP routers must have a path to the external EBGP router either through an IGP or a static route.
Notes: 不是路由器的下一跳，而是AS的下一跳

## Slide 30
Routers A and C have established an EBGP session
  The NEXT_HOP attribute for routes advertised between these peers is set to the remote peer’s IP address
    On A, the NEXT_HOP attribute for 150.10.0.0 is set to 10.10.20.2
    On C, the NEXT_HOP attribute for 170.10.50.0 is set to 10.10.20.1
Routers A and B have established an IBGP session
  On B, the NEXT_HOP attribute for the external route to 150.10.0.0 is not changed, i.e. 10.10.20.2 or C’s IP address
    Remember: B must have a route to 10.10.20.0 in its routing table or it will drop packets destined for 150.10.0.0 even though it knows about it through BGP.
AS 100
150.10.0.0
10.10.20.1
10.10.20.2
AS 200
EBGP
IBGP
170.10.50.0
A
B
C
Notes: AS内部传输路由信息时不改变下一跳的值
AS之间传输时如果其间没有直接到达的路径，则需要修改下一跳的值。

## Slide 31: MULTI_EXIT_DISC(MED)
Multi-Exit Discriminator: an optional non-transitive attribute
MED specifies the preferred route external ASes should take into the local AS.
  The receiving router will not propagate the MED to any other BGP peers, but resets the MED attribute to zero.
  The MED can be used by an AS to influence the outbound decision of another AS.
  The lower the value of the MED, the more preferred the route into the advertising AS.
  By default, the receiving router will only compare MEDs received from the same AS.
Notes: AS有多个出口时，用来配置以选择路径。
画图，要走流量的AS之间路径配较低值，接受方比较（缺省同一个AS）不同路由的MED值，其在AS内部都传播，但是不跨AS传播。不同AS来源的路径也可以比较，只要配上了：always-compare-med

## Slide 32: LOCAL_PREF
LOCAL_PREF: an well-known discretionary attribute
LOCAL_PREF is used by a BGP router to inform its IBGP peers the degree of preference for the advertised route.
  Used to force IBGP peers to prefer one exit point over another when routing to a particular destination network.
  Unlike the MED, the higher the LOCAL_PREF the more preferred the route.
  LOCAL_PREF is not advertised to EBGP peers
Notes: 只对本AS起作用，取值大的路由更优先。缺省为100
用于本地局部施加影响

## Slide 33: ATOMIC_AGGREGATE
ATOMIC_AGGREGATE: a well-known discretionary attribute
ATOMIC_AGGREGATE is used by a BGP router to alert BGP peers that multiple destinations have been grouped into a single update.
Notes: 发生在路由聚合时

## Slide 34: AGGREGATOR
AGGREGATOR: an optional transitive attribute.
  When configuring address aggregation, you can also configure the router to include its router ID and local AS number along with the supernet route.
  This attribute enables ISP administrators to determine which BGP router is responsible for a particular instance of aggregation.
  Tracing a supernet to its original "aggregator" may be necessary for troubleshooting purposes.

## Slide 35: Cisco Defined Attributes
The last three attributes are as follows:
  COMMUNITY—optional transitive attribute
    Used to apply one routing policy to all destinations that belong to the community.
  ORIGINATOR_ID—optional non-transitive attribute that is beyond the scope of the BSCN exam.
    Used by Route Reflectors to identify the originator of a route and eliminate routing loops.
  CLUSTER_LIST—optional non-transitive attribute that is beyond the scope of the BSCN exam.
    It is used to specify a Cluster ID when multiple router reflectors are configured for redundancy purposes
    NOTE: Be sure to download Cisco’s PDF file: Configuring BGP. It explains these attributes (and much more) in great detail.
Notes: 一组有相同性质的目的地。
团体号：
No-export：不到联盟或AS之外的路由器
No-advertise：不到所有别的BGP路由器
Local-AS：不到AS之外

## Slide 36: One Last Attribute!!
A proprietary attribute of Cisco: WEIGHT.
  This attribute is local to the router and is not propagated. Therefore, there’s no Attribute Type Code.
  Similar to LOCAL_PREF, the router will choose the path with the highest WEIGHT.
  The value of the attribute is a 16 bit number from 0 to 65,535.
    Paths that are originated by the router, by default, have a WEIGHT of 32,768 and all other paths have a WEIGHT of 0.
  You can see this attribute when issuing the show ip bgp command.

## Slide 37: Attributes and BGP Decisions
How does BGP pick the best path?
In general, it works like this:
  When BGP has multiple paths to the same destination, only one path can be selected.
  Therefore, when BGP receives multiple routes to the same destination with the same path attributes specified, it will pick the best path based on how their values are weighted.
But what if the two routes do not specify the same path attributes?
  For example, one route specifies a MED while the other route specifies only the well-known mandatory attributes.
  Unlike EIGRP and IGRP, there’s no way to form a composite metric. Therefore, BGP evaluates each attribute in a specific order.

## Slide 38: Route Selection Decision Process
If an internal route is not synchronized and synchronization is enabled, do not consider it
If the next hop address specified in the NEXT_HOP attribute is not reachable, do not consider it.
Choose the route with the highest WEIGHT (Cisco proprietary)
If WEIGHT is equal, choose the path with the highest LOCAL_PREF
If LOCAL_PREF is equal, choose the path originated by the local router
If the local router did not originate one of the paths with equal LOCAL_PREF, then choose the path with the shortest number of AS hops indicated by the AS_PATH attribute.
Notes: 5：本地路由优先

## Slide 39: Route Selection Decision Process
If routes have the same number of AS hops, choose the path based on the ORIGIN attribute: IGP over EGP; EGP over Incomplete
If routes have the same ORGIN, choose the path with the lowest MED
If MED is same or irrelevant, choose an EBGP path over an IBGP path
If no routes through EBGP, choose the path with the lowest IGP metric to the BGP next hop.
If only EBGP routes remain, then load balance if configured.
If no load balancing configured, the choose the route with the lowest BGP router ID.

## Slide 40
Route
Synchronized?
Do Not
Consider
No
Next Hop
Reachable?
Yes
Highest
WEIGHT?
Yes
No
Highest
LOCAL_PREF?
Install
Route
Yes
No
Originated by
local router?
Yes
No
Shortest
AS_PATH?
Yes
No
Lowest
ORIGIN?
Yes
No
Lowest
MED?
Yes
No
Any EBGP
Paths?
Yes
No
Load Balance
Enabled?
Lowest
IGP Metric
Yes
No
Lowest BGP
Router ID
Yes
No

## Slide 41: Synchronization
The synchronization rule states:
  A BGP router can not advertise routes learned from an IBGP peer to other BGP peers unless the local router also has learned about the route via an IGP protocol.
  Router B would continue to send traffic for 10.10.10.0 to Router C, but Router C cannot route the traffic to Router A because it has not learned about 10.10.10.0 via an IGP. This situation is called a “black hole.”
  Router C can learn about the route in one of three ways:
      Directly connected (not possible in graphic below)
      Statically configured
      Dynamic IGP routing protocol
AS 300
150.10.0.0
AS 200
EBGP
IBGP
170.10.50.0
B
C
Non-BGP Router
AS 100
10.10.10.0
A
EBGP

## Slide 42: Overriding Synchronization
As seen in the previous slide, synchronization is absolutely crucial in some situations.
  However, synchronization can be safely turned off if...
    All transit routers in the AS are running fully meshed IBGP
      In the previous graphic, the two transit routers are not physically connected.
    or..
    The AS is a non-transit AS
  In the Cisco IOS, synchronization is on by default. To turn it off, use the no synchronization routing command.
Notes: crucial ：关键